## Slide 1: Introduction to NMR
Konstantin Ivanov (Novosibirsk, Russia)
4th NMR Meets Biology Meeting
Khajuraho, India, 16-21 December 2018

## Slide 2: Outline
Angular moment (spin) and magnetic moment;
Magnetic resonance phenomenon;
Bloch equations;
NMR pulses;
FID, Fourier transform, 1D-NMR, 2D-NMR;
T1 and T2 relaxation.

## Slide 3: Angular momentum and magnetic moment
In NMR we deal with spin magnetism. What is ‘spin’?
Charged nucleus (or electron) is spinning:
there is angular momentum (spin) and magnetic moment
attention: this is a simple view, which is not (entirely) correct
So, μ is proportional to a.m.; when a.m. is measured in ħ units
Quantum mechanics: this is not entirely correct (we are wrong by the g-factor)!
q
The electric current for a charged
particle moving around
The magnetic moment is

## Slide 4: Angular momentum and magnetic moment
Furthermore, QM tells us that S is quantized: angular moment measured in ħ units cannot be an arbitrary number
Stern-Gerlach experiment:
The beam of particles is deflected by inhomogeneous field
Reason: intrinsic magnetic moment (spin) of particles
In contrast to the classical expectation the distribution of the μ-vector is not continuous!
Spin is quantized

## Slide 5: Angular momentum and magnetic moment
Furthermore, QM tells us that S is quantized: angular moment measured in ħ units cannot be an arbitrary number
S is integer (0, 1, 2, …) or half-integer (1/2, 3/2, 5/2, …) and |S|={S(S+1)}1/2
Projection of S onto any axis in space varies in steps of 1 from – S to S
Spin-½ particle (1H, 13C, 15N, 19F, 31P…): possible projections are ±1/2
Spin-1 particle: possible projections are –1, 0, 1
When discussing spin-½ particles we can use a simplification (and forget about QM): spin magnetization is a classical vector in the 3D-space, which is changing by moving in external fields and due to spin relaxation
As we can see from the density matrix description, this is correct (but only for two-level systems!): fictitious spin description

## Slide 6: Magnetic resonance: classical viewpoint
Motion of a classical magnetic moment in a constant magnetic field B0
Magnetic moment is
γN is the gyromagnetic ratio (or magnetogyric ratio)
We obtain a torque:
These equations tell us that:
|J|=const; the J-vector is rotating about B0 at a frequency ω0=|γN|B0
This is precession of magnetic moment
The direction is given by the γN sign
What happens to the magnetic moment if we apply an oscillating field?
Typically this field is much weaker than B0: it does nothing except for some special cases
B0
μ, J
torque

## Slide 7: Magnetic resonance: classical viewpoint
Let us apply an oscillating field perpendicular to B0: B┴=2B1cos(ωt)
To account for the effect of this field we can go
to the rotating frame:
Linear polarized field = 2 circularly polarized fields: two vectors rotating with the same speed in opposite directions
At high w the vector, which rotates with double frequency can be neglected. This is (usually) Ok for the description of resonance
x
y
x´
y´
z=z´
wt
If a is a constant vector in the RF, in the LF we obtain
x
y
Lab frame
x´
y´
Rot. frame

## Slide 8: Magnetic resonance: classical viewpoint
What happens to the transverse field:
Linear polarized field = 2 circularly polarized fields: two vectors rotating with the same speed in opposite directions
Graphical representation in both frames:
At high w the vector, which rotates with double frequency can be neglected. The other vector does not move. This is (usually) Ok for the description of resonance
x
y
Lab frame
x´
y´
Rot. frame

## Slide 9: Magnetic resonance: classical viewpoint
Equation of motion in the rotating frame
By taking derivative we obtain:
Equation of motion in the rotating frame
Still the same equation but the new field equals to
Superposition of the new B0 and B1-fields gives a constant effective field Beff
Here d/dt is the time derivative in the rotating frame
Here the components of J change and the basis vectors {i, j, k} also change with time

## Slide 10: Magnetic resonance: classical viewpoint
The effective field is the following vector
Precession frequency is
If w=w0 the precession axis is the x-axis => variation of Jz reaches its maximum. This variation rapidly decays with w going to zero at |w–w0|>>w1
Resonance condition: w = (free precession frequency). Weak B1 is important!
Frequency range (given by γN): radio-frequency, i.e., 300 MHz for 1H @ 7 Tesla
Resonance width is given by condition |w–w0|≈w1. If w1>>|w–w0| the effective field is nearly parallel to the x-axis – we are at resonance!
At resonance the precession frequency is w1. If we switch on the resonant oscillating field for time period of τp the flip angle of magnetization is
B0–w/|gN |
B1
Beff
x´
z

## Slide 11: Magnetic resonance: simplified quantum viewpoint
The energy of interaction of the spin with an external field is
If B0 is parallel to the Z-axis
The degeneracy of the spin levels is lifted
Fermi’ golden rule tells us that there is a resonance when ω=ω0
Absence of MF
Presence of MF
E=|γN|B0/2
E= –|γN|B0/2
Periodic perturbation

## Slide 12: Macroscopic spin magnetization
Up to now we discussed a single spin ½, which is never the case in NMR
At thermal equilibrium we have almost the same amount of spins pointing up and down: the energy gap between the spin levels is much smaller than kT
We work with net magnetization of all spins; at equilibrium this is a vector parallel to B0 (longitudinal magnetization)
However, we do not measure the longitudinal component, but rotate M with RF pulses to obtain transverse magnetization and measure the signal from M┴
B0
Nuclear
paramagnetism:
the induced field is parallel to B0

## Slide 13: T1 and T2 relaxation
Relaxation is a process, which brings a system to thermal equilibrium. Physical reason: fluctuating interaction of spins with molecular surrounding
For spins this means that Mz=M||=Meq and M┴=0
There are two processes, which are responsible for relaxation
  Longitudinal, T1, relaxation: Meq is reached at t~T1:
  Transverse, T2, relaxation: magnetization decays to zero at t~T2:
Generally, T1≠T2.
Taking all that into account we can write down equations describing precession+relaxation

## Slide 14: Bloch equations and FID
We write down equations describing precession and add relaxation terms
Now we can describe simplest NMR experiments. Example:
Mz is flipped by 90 degrees by a resonant RF-pulse: φ=ω1τp=π/2
It starts rotating about the z-axis and decaying with T2
We detect My (or Mx) and collect the Free Induction Decay (FID)
x
y
z
Free Induction Decay
t
0
1
-1
How to obtain the spectrum?
ω1τp

## Slide 15: Fourier Transform NMR
How do we obtain the spectrum – by performing the Fourier transform
Some examples
t
0
1
-1
Fourier transform
w
time domain f(t)
frequency domain g(ω)
δ-function, single freq.
Lorentzian at zero freq.
Lorentzian at ω0 freq.
FT
FT
FT
g(ω) = f(t) cos(ωt)dt


0

## Slide 16: Fourier Transform NMR
How do we obtain the spectrum – by performing the Fourier transform
Some examples
FT can be performed in a fast and efficient way (FFT algorithm)
t
0
1
-1
Fourier transform
g(ω) = f(t) cos(ωt)dt


0
w
time domain f(t)
frequency domain g(ω)
Inverse FT gives g(ω) from the FID signal
FT
IFT
Widths of g(ω) and FID(t) are inter-related: δt~1/δω

## Slide 17: Fourier Transform NMR
A few words about pulses
RF-synthesizer produces a signal oscillating at the spectrometer reference frequency ωref:
Gating: the signal passes through the transmitter only for certain periods of time => we obtain an RF-pulse
Parameters of the pulse:
frequency ωref
strength B1 and duration τp provide the flip angle φ = |γN|B1τp = ω1τp
phase: ψ=0 (x-pulse), ψ=π/2 (y-pulse), ψ=π (–x-pulse), ψ=3π/2 (–y-pulse)
The phase is time-dependent and can be precisely controlled

## Slide 18: Fourier Transform NMR
A few words about FID detection
We measure the signal comparing it to the reference frequency ωref (recording oscillations at ~100 MHz frequency would be a disaster)
Problem: no sensitivity to the sign of Ω0 (ωref greater or smaller than ω0)
The solution is quadrature detection: the receiver provides a phase-shifted signal to obtain the information about the sign
We introduce ‘complex magnetization’, which contains full information
Fourier transformation yields
Yet phasing is a problem

## Slide 19: Fourier Transform NMR
Fourier transformation yields
Real and imaginary part of the signal (when C is real)
Generally, C=|C|eiψ is a complex number because of a phase shift of the pulser and receiver
By varying the phase we can obtain the Lorenzian or purely dispersive line
The phase can be set and then kept the same
L(Ω)
D(Ω)

## Slide 20: Back to relaxation
Before talking about 2D-NMR let us briefly discuss T1 and T2
Origin of T1 and T2
Relaxation and molecular motion
Measurement of the relaxation times

## Slide 21: T1-relaxation
T1-relaxation: precession in the B0 field and a small fluctuating field Bf (t)
The precession cone is moving
Eventually, the spin can even flip
Spin flips up-to-down and down-to-up have slightly different probability (Bolztmann law!): Mz goes to Meq≠0
General expression for the transition rate
B0
B0+Bf (t)
B0
Noise spectral density at the transition frequency
τc is the motional correlation time

## Slide 22: T2-relaxation
T2-relaxation: kicks from the environment disturb the precession
Different spins precess differently and transverse net magnetization is gone
Generally the T2-rate
Two contributions:
Adiabatic and non-adiabatic (T1-related)
Dephasing

## Slide 23: Noise spectral density
Simple example: spins relaxed by fluctuating local fields, Bf (t)=0
However, the auto-correlation function is non-zero
Typical assumption
Lorentzian-like noise spectral density
Exponential auto-correlation function
τc comes into play
time
t
t

## Slide 24: Expressions for T1 and T2
Simple example: spins relaxed by fluctuating local fields, Bf (t)=0
The auto-correlation function is non-zero
General expressions for T1 and T2
This dependence is explained by the J(ω) behavior

## Slide 25: Inhomogeneous linewidth
Problem: we need to discriminate two contributions to T2
Decay of the NMR signal also proceeds due to static inhomogeneities in the precession frequency w0. This can be due to external field gradients and local static interactions.
Resulting rate the signal decay
The first two contributions are the same for all the molecules and thus define the homogeneous linewidth.
The last contribution defines the inhomogeneous linewidth.
In solids usually
w
D
NMR
spectrum
Reason: δω·δt~2π

## Slide 26: T2-measurement: spin echo
Large inhomogeneous linewidth means very fast dephasing of the spin
However, dephased magnetization can be focused back by pulses
Explanation: let us divide system into isochromates having the same frequency w0. Their offsets are Dw=w0–w. At certain time they all have different phases
But at t=2t all have the same phase: there is an ‘echo’!
The spin echo signal decays with T2
p/2
p
echo
0
t
2t
t
x
y
t=0
j=0
x
y
j=Dwt
x
y
j=p–Dwt+Dw(t–t)
x
y
t=2t
j=p
pulse sequence p/2x - t - px

## Slide 27: T1-measurement: inversion-recovery
Determination of T1 is often quite important as well
Standard method is inversion-recovery
First we turn the spin(s) by pulse (usually p/2 or p) and then look how system goes back to equilibrium (recovers z-magnetization). If the pulse is a p-pulse magnetization will be inverted (maximal variation of m-n) and then recovered
Equation for Mz is as follows:
The kinetic trace (t-dependence) gives T1-time
To detect magnetization at time t one more p/2-pulse is applied, the sequence is then px - t (variable) - px/2 - measurement
Spin echo can be used for detection as well, the pulse sequence is then px - t (variable) - px/2 - t - px - t - measurement
The sequence should be repeated with different delays t
1
–1
t

## Slide 28: 1D-NMR
1D-NMR experiment (simplest case)
Why is it not enough?
preparation - detection
S(t)
FT
S(ω)
For large proteins it is really hard to assign NMR signals and to obtain information from the spectra!
Too many peaks  Spectrum is a mess!

## Slide 29: 2D-NMR
2D FT-NMR
implementation
Preparation evolution mixing detection
t1
tm
t2
S(t1,t2)
FT1, FT2
S(ω1,ω2)
Idea: adding a second dimension for improved resolution
t2 – direct domain
t1 – indirect domain
It is up to you how to design preparation and mixing: decide, what you want to know about your molecules!

## Slide 30: 2D-NMR spectrum of a protein
Contour plot: topographical lines
In 2D the peaks become resolved

## Slide 31: Direct and indirect domain
Direct time domain (acquisition, t2): FID detection
Indirect time domain (evolution time, t1 in 2D): FIDs are collected for different t1 times
t1
The FID depends on the evolution in t1: the signal is 'modulated' with ω1
For simplicity here the frequency ω is the same in t1 and in t2
t2=0
FT (t2)
t2
FT (t1)
w2
w1

## Slide 32: Cross-peaks and diagonal peaks
Simple example: SCOTCH experiment
Spin COherence Transfer in (photo) CHemical reactions
Reaction A B with a proton at ωA in A which resonates at ωB in B.
hν
t1
t2
l
i
g
h
t
M magnetization evoilves with the frequency ωA in t1. After the light pulse, the frequency changes to ωB.
FT provides a 2D spectrum with a peak at ωA in F1 and ωB in F2
FT
The cross-peak comes from A → B and ωA≠ωB
When conversion A → B is incomplete the diagonal peak stays

## Slide 33: Example: NOESY experiment
tm
t2
Cross-peaks come from NOE during the mixing period
SY = SpectroscopY
t1
How does it work?
I1z  –I1y  –I1y  –I1z  –I2z  I2y
Transverse magnetization has gone from spin 1 to spin 2
The efficiency of transfer is (simplified)
sin(ω1t1) *sin(ω2t2)
A cross-peak will appear in the NOESY-spectrum
The cross-peak gives information on NOE  distance between the spins
The same method can be used to study chemical exchange (EXSY)
π/2x t1 π/2x NOE π/2x
π/2 π/2 π/2
ω1→
ω2→
Ω1 Ω2

## Slide 34: Summary
NMR is working with magnetic moments of nuclei (originating from their spins)
Simple theory (Bloch equations) allows one to understand basic experiments
1D & 2D NMR concepts are introduced